## Slide 1: HAZARDOUS WASTE MANIFESTS
Notes: Objectives:
Review the applicability of the hazardous waste manifest requirements.
Discuss the general requirements of the manifesting regulations.
Examine generator, transporter, and TSDF issues.
Discuss bulk shipment by water and rail shipment situations.
Review export and import requirements.
Review LDR and Universal Waste requirements as they affect use of manifests.

## Slide 2: APPLICABILITY
Generator that transports, or offers for transport, hazardous waste for off-site treatment, storage or disposal
Transporters of hazardous waste
Treatment, storage, and disposal facilities
Exception: Reclamation of SQG waste under contract
Notes: Manifest requirements apply to hazardous waste generators, transporters, and treatment, storage and disposal facilities.
Primary responsibility for preparing the manifest falls upon hazardous waste generators. Conditionally exempt SQGs are exempt from manifest requirements.
Manifest requirements also do not apply to SQGs where waste is reclaimed under a contractual agreement that specifies the type of waste and frequency of shipments, the vehicle used to transport the waste is owned and operated by the reclaimer, and the generator maintains a copy of the reclamation agreement for 3 years after termination or expiration of the agreement.

## Slide 3: GENERAL SCHEME
Generator prepares manifest, designates destination facility
Signed manifest accompanies each waste transfer
When waste reaches destination, signed manifest returned to generator
Exception report sent to EPA if signed manifest not received within 45 days of initial transporter receiving waste
All entities subject to manifest requirements must retain copies for 3 years
Notes: The generator prepares the manifest, and is responsible for accurately completing each section of the form.
The manifest must consist of at least the number of copies that will provide the generator, each transporter, and the owner or operator of the designated facility with one copy for their records, and a remaining copy to be returned to the generator.
The generator must designate a destination facility, and can designate an alternate destination facility.
Upon each transfer of the waste, the manifest must be signed and dated by the party taking possession of the waste.
If a generator of greater than 1000 kilograms of waste per calendar month does not receive a manifest signed by the owner or operator of the destination facility with 35 days of the initial transfer of the waste, s/he must determine the status of the waste.
A generator of greater than 1000 kilograms of waste per calendar month must submit an exception report if a manifest signed by the destination facility is not received within 45 days of initial transfer of the waste.
Records of manifests must be maintained for 3 years.

## Slide 4: OBTAINING MANIFESTS
Consignment state supplies and requires use -- generator must use
Consignment state does not supply; generator state supplies and requires use -- generator must use
Neither supplies -- generator may use manifest from any source
All state manifests do not look alike
Some state waste codes are different from EPA waste codes (state waste codes are permissible)
Notes: The manifest form may be supplied and required to be used by the consignment state, or, where that is not the case, the state in which the generator is located. If neither supplies the manifest, the generator may obtain the form from any source.
All state manifests do not look alike. Therefore, it is important to verify that they contain the required information.
In addition, some states use waste codes that are different from those developed by EPA. Federal regulations do not require that federal waste codes be used, although state regulations might.

## Slide 5: GENERATOR ISSUES
Must prepare manifest
Must sign and obtain date of acceptance by initial transporter
Retain copy for 3 years or until designated facility returns signed copy, which must be retained 3 years
Special cases: Bulk shipments by water; Rail shipments
Notes: A generator must prepare a manifest before s/he transports, or offers for transportation, hazardous waste for off-site treatment, storage or disposal.
The generator must:
  - Sign the manifest
  - Obtain signature and date of acceptance from initial transporter
  - Retain copy for 3 years or until designated facility returns signed copy, which must be retained for 3 years.
Bulk shipments by water and rail shipments have special requirements. Copies of the manifest are not required for each transporter.

## Slide 6: BULK SHIPMENT BY WATER
Bulk shipments within U.S. solely by water
Generator must send 3 signed and dated copies to:
  Designated facility, or
  Last water transporter if exported by water
Notes: For bulk shipments in the U.S., solely by water, the generator must send three signed and dated copies of the manifest to:
  - The designated facility, or
  - The last water transporter, if the waste is exported by water
  - Copies of the manifest are not required for each transporter.
Designated facility must return copy of manifest to generator.
In case of export by water, generally, the last water transporter in the U.S. forwards the manifest to subsequent transporters or the consignee in the destination country. (See discussion of export).

## Slide 7: RAIL SHIPMENT
Rail shipment within U.S. that originates at site of generation
Generator must send 3 signed and dated copies to:
  Next non-rail transporter, or
  Designated facility, or
  Last rail transporter to handle waste in U.S. if exported
Notes: For rail shipments within the U.S. that originate at the site of generation, the generator must send 3 signed and dated copies of the manifest to:
  - The next non-rail transporter, or
  - The designated facility, or
  - The last rail transporter to handle the waste in the U.S., if exported by rail.
Subsequent non-rail transporter or designated facility must comply with normal manifest requirements.
In case of export by rail, generally, the last rail transporter in the U.S. forwards the manifest to subsequent transporters or the consignee in the destination country. (See discussion of export).

## Slide 8: TRANSPORTER ISSUES
Any hazardous waste accepted must be accompanied by signed manifest
Must sign, date, and return copy prior to transporting
Manifest must accompany hazardous waste
Deliver waste to designated facility, alternate, designated transporter, or designated place outside U.S.
Obtain signature and date upon delivery to designated facility or transporter
Retain signed manifest for 3 years from acceptance
Notes: All hazardous waste must be accompanied by properly completed manifest.
Transporters must sign, date, and return a copy of the manifest to the generator prior to transporting waste.
The transporter must deliver the entire quantity of hazardous waste accepted from the generator to:
  - The designated facility listed on the manifest
  - The alternate designated facility, if waste cannot be delivered to the designated facility
  - The next designated transporter
  - The place outside the U.S. designated by the transporter.
If waste cannot be delivered as specified, the transporter must contact the generator for direction and revise the manifest accordingly.
The transporter must obtain the date of delivery and signature of the transporter, or owner or operator of the designated facility.
The transporter must retain one copy of the manifest for 3 years from the date the waste was accepted, and provide the remaining copies to the subsequent transporter or designated facility.

## Slide 9: TSDF ISSUES
Must sign and date manifests accompanying hazardous waste
Must note discrepancies, attempt to reconcile
Send copy of signed manifest to generator within 30 days
Retain copy of manifest for 3 years from delivery
Notes: Where TSDF receives hazardous waste accompanied by manifest, the owner or operator must:
  - Sign and date each copy of manifest
  - Note significant discrepancies
  - Provide the transporter with one copy of manifest
  - Within 30 days, send signed copy of the manifest to the generator
  - Retain a copy for 3 years from date of delivery.
Manifest discrepancies include a difference in the quantity or type of hazardous waste designated on the manifest and quantity or type of waste actually received. Incorrectly or inadequately identified waste is also significant.
Significant discrepancies include:
  - Bulk Waste - Variations greater than 10 percent in weight;
  - Batch Waste - Any variation in piece count.
The owner or operator must attempt to reconcile discrepancies with the generator and/or transporter (verify letters, notes). If not resolved within 15 days, the owner or operator must notify EPA of the discrepancy and provide a copy of the manifest (verify letter).

## Slide 10: LDR ISSUES
Generator managing restricted waste must provide notice to treatment or storage facility that waste does or does not meet treatment standards
  If waste meets treatment standards, certification also required
Varying forms of notification and certification required under 268.7
LDR notification and certification are not part of manifest but generally accompany manifest
Notes: Hazardous waste generators managing an LDR restricted waste must provide notice to the TSDF that the waste does or does not meet the applicable treatment standard.
If the waste meets the treatment standard, certification of such is also required. (Debris that does not contain hazardous waste is not subject to notice or certification).
Written notice that waste does not meet standard must include: 1) waste ID number; 2) constituent data (specified wastes) and category (WW/NWW); 3) manifest number; 4) whether waste is debris; and 5) waste analysis data (where available).
Written notice that waste does meet standard must include all but debris information noted above.
Certification that waste meets applicable standards must include certification statement (268.7(2)(ii)) signed by authorized representative.
If waste subject to LDR exemption, notice of such must be provided from generator to TSDF.
Notice and certifications not part of manifest, but often accompany manifest.
Records of notices and certifications must be keep for 5 years.

## Slide 11: EXPORT FRAMEWORK
Export or import of hazardous waste subject to: 1) manifest requirements or 2) universal waste standards, to or from designated OECD countries for recovery, is subject to 262 Subpart H in lieu of existing export/ import requirements
Subpart H imposes tracking document requirements upon exporter and importer
Notes: The requirements of 262, Subpart H apply to:
  - Export or import
  - Hazardous wastes subject to manifest or universal waste standards
  - To or from OECD countries designated under 262.58(a)(1) and (2)
  - For recovery only.
Notification and consent are required prior to export or import for recovery.
A contract is required for transfrontier movement of amber- and red-list wastes.
Parties subject to contract provisions must ensure tracking document accompanies transfrontier shipment of amber or red wastes from initiation of shipment until it reaches the final recovery facility.

## Slide 12: EXPORTS
Primary exporter of hazardous waste must generally comply with manifest requirements, except:
  Consignee replaces designated or alternate facility
  Manifest must identify point of departure from U.S.
  Consignee must confirm in writing delivery of waste and note discrepancies
  Special requirements where delivery not possible
  EPA Acknowledgment of Consent must accompany waste
  Special exception report requirements
Notes: Primary exporters must generally comply with manifest requirements, except that : consignee replaces designated facility; alternate consignee replaces alternate designated facility; point of departure identified on manifest; Acknowledgment of Consent must be attached to manifest, and certification must note shipment conforms to Consent; and exporter must require consignee to confirm delivery (signed copy of manifest sufficient).
Where shipment cannot be delivered, primary exporter must: notify EPA of change to new consignee and obtain Acknowledgment of Consent; or, instruct transporter to return waste to primary exporter and have transporter revise manifest accordingly.
Primary exporter must file exception report if: s/he does not receive signed manifest from transporter noting date and place of departure from U.S. within 45 days of initial acceptance; s/he does not receive written confirmation from consignee within 90 days of initial acceptance; or the waste is returned to the U.S.

## Slide 13: IMPORTS
Generally subject to manifest requirements
Minor changes to address import of waste
Notes: Importer must provide name and address of the foreign generator, and importer’s name, address, and EPA ID number on the manifest.
In place of the generator signature, the U.S. importer or agent must sign and date certification.
An importer must obtain a manifest from the consignment state if that state supplies manifests and requires use of the state-issued manifest. Otherwise, the importer can obtain the form from any source.

## Slide 14: UNIVERSAL WASTES
Wastes include certain batteries, pesticides, and mercury thermostats
Small quantity handlers are not required to keep records of shipments
Large quantity handler must keep a record of each shipment
Transporters must comply with DOT requirements if hazardous material
Destination facilities must keep record of each shipment received
Notes: Universal wastes include: hazardous waste batteries including nickel-cadmium batteries and lead acid batteries not managed under Part 266; hazardous waste pesticides including those banned from use, obsolete, damaged, or subject to recall (excluding those recalled pesticides and products managed in compliance with Part 262.70); and hazardous waste mercury thermostats. (See 40 C.F.R. 273.6).
Small quantity handlers of universal wastes (accumulate less than 5000 kgs at any time -- SQHUW) are not required to keep records of shipments of universal wastes. However, SQHUW that send wastes off-site must comply with DOT requirements if wastes are hazardous materials.
Large quantity handlers of universal wastes (accumulate 5000 kgs or more at any time -- LQHUW) must document shipments sent and received (e.g., log, invoice, manifest, bill of lading, etc.) and keep records for 3 years. LQHUW also must comply with DOT if wastes are hazardous materials.
Transporters must comply with DOT requirements if waste is hazardous material.
Destination facilities must maintain record of each shipment of universal waste received (e.g., log, invoice, manifest, bill of lading, etc.) for 3 years.