## Slide 1
WASTE MINIMIZATION
and
POLLUTION PREVENTION
Notes: Objectives:
Understand the terms waste minimization and pollution prevention.
Review RCRA requirements regarding waste minimization and pollution prevention.
Examine relevant policies, including the role of the inspector in promoting waste minimization.
Discuss outreach.

## Slide 2: Terminology
Pollution Prevention
Waste Minimization
Notes: Pollution Prevention is source reduction in the manufacturing process through process changes, chemical substitution, better controls on the process, closed loop recycling within the process, or any practice that "reduces the amount of any hazardous substance, pollutant or contaminant entering any waste stream or otherwise released into the environment (including fugitive emissions) prior to recycling, treatment or disposal..." (Pollution Prevention Act of 1990)
Waste Minimization is multi-media source reduction and recycling except for recycling involving combustion (i.e. recycling for energy recovery).
There is a movement to try to eliminate the term waste minimization because it is thought of to only apply to RCRA. Since true waste minimization must be looked at from a multi- media perspective you should not restrict it to any one regulatory program.

## Slide 3: PP/WM LEGISLATION
• HSWA § 1003 (a) (6)
• HSWA § 3002 and §3005
• Pollution Prevention Act of 1990
Notes: EPA is required, under the Hazardous and Solid Waste Amendments of 1984 (HSWA), to protect the environment by "minimizing the generation of hazardous waste and the land disposal of hazardous waste by encouraging process substitution, materials recovery, properly conducted recycling and reuse, and treatment;" HSWA §1003 (a) (6).
HSWA sets forth three basic waste minimization requirements for generators and treatment, storage and disposal facilities. They are:
  1. That hazardous waste generators submit waste minimization information as part of the biennial reports (§3002 (a)(6));
  2. That generators certify on the manifest that they have a waste reduction program in place (§3002 (b));
  3. That as a permit requirement, all TSDFs must certify at least annually that they have a waste reduction system in place (§3005 (h))

## Slide 4: WASTE MANAGEMENT HIERARCHY
Source Reduction
Recycling
Treatment
Disposal
Most
Environmentally
Beneficial
Least
Environmentally
Beneficial
Notes: This long quotation from the Act boils down to what is known as the waste management hierarchy.
This simply lays out that source reduction is preferable to recycling which is preferable to treatment which is preferable to disposal.
For the sake of definitions, the term "Pollution Prevention" refers to the top level of the hierarchy: source reduction; the term "Waste Minimization" refers to the top two level of the hierarchy, both source reduction and recycling.

## Slide 5: POLLUTION PREVENTION STRATEGY
  "EPA does not view pollution prevention as an exotic activity standing apart from the Agency's primary mission; rather the goal is to incorporate prevention into every aspect of the Agency's operations in programs and regional offices."
EPA Pollution Prevention Strategy
November, 1990
Notes: This statement translates into a mandate from the Administrator, William Reilly, that we work pollution prevention into all aspects of EPA's work, whether it be research, writing regulations, or enforcement.

## Slide 6: POLLUTION PREVENTION IN ENFORCEMENT SETTLEMENTS
"It shall be a policy of the EPA to favor pollution prevention and recycling as a means of achieving and maintaining statutory and regulatory compliance and of correcting outstanding violations when negotiating enforcement settlements."
Interim EPA Policy on the Inclusion of Pollution Prevention and Recycling Provisions in Enforcement Settlements
February 25, 1991, Memorandum from James M. Strock,
Policy on Use of Supplemental Environmental Projects in EPA Enforcement Settlements (May 1995)
Notes: The Office of Enforcement has written this policy to provide a standardized method to include pollution prevention into settlements in all media programs.
In May 1995, EPA published a Policy on the Use of Supplemental Environmental Projects (SEPs) in EPA Enforcement Settlements. This policy supersedes the 1991 policy and defines SEPs, establishes legal guidelines, defines acceptable and unacceptable SEP categories, as well as implementation criteria and procedures.
EPA has also developed SEP guidance and a SEP database, both of which are available on the internet (see http://es.inel.gov/oeca/sep/).

## Slide 7: ROLE OF THE INSPECTOR
POLICY STATEMENT
"The Role of RCRA Inspectors in Promoting Waste Minimization"
OSWER Directive # 9938.10 September 12, 1991
Notes: The Office of Waste Programs Enforcement issued this policy last September to define the Role of the Inspector in Waste Minimization. You should have that in front of you. The policy is pretty self explanatory but we will discuss key points.

## Slide 8: DETERMINE COMPLIANCE
• Check Manifest (40 CFR §262, Appendix)
1. Ask for written Waste Minimization Plan.
2. If no written plan, ask for oral description.
3. Check for "program in place" on site.
Notes: Using the authority of HSWA §3002 and §3005, EPA promulgated regulations addressing theses issues in the 40 CFR under §262.20; §262.41; §262.56; §§264 and 265.75; and §264.73.
These regulations simply say that generators must certify on the Manifest that they have a waste minimization program in place.
  "If I am a large quantity generator, I certify that I have a program in place to reduce the volume and toxicity of waste generated to the degree I have determined to be economically practicable and that I have selected the practicable method of treatment, storage or disposal currently available to me which minimizes the present and future threat to human health and the environment; OR, if I am a small quantity generator, I have made a good faith effort to minimize my waste generation and select the best waste management method that is available to me and that I can afford." (40 CFR §264, Appendix)
• You should always check to make sure that that statement was signed by the right person.
• You should always check to see that they do have a waste minimization plan that it is being implemented. We cannot judge the adequacy of a program but we can confirm its existence. Many states may have more enforceable planning regulations. Follow those.

## Slide 9
• Check Biennial Report and Operating Record
1. Generators must submit description of
WM activities in biennial report.
(40 CFR §262.41(a), 264/265.75 (h) & (j))
2. Certification in permittees' operation
record. (40 CFR §264.73 (b) (9))
• Check Permit Conditions and Enforcement
Settlements
DETERMINE COMPLIANCE (cont.)
Notes: Any generator that ships waste off-site or treats waste on-site must submit waste minimization language with the biennial report. The report should contain a:
- Description of efforts undertaken during the year to reduce the volume and toxicity,
- Description of changes in volume and toxicity actually achieved,
- Certification signed by generator or authorized representative.
You should check to make sure that information is included in the report. Once again, many states have more stringent reporting requirements. If those apply, make sure they are followed.
Permitted facilities should include annual certification of waste minimization program in place. On May 28, 1993, OSW published "Interim Final Guidance to Hazardous Waste Generators on Elements of a Waste Minimization Program" (58 FR 31114, 5/28/93) to help explain what a good waste minimization program should include. This is, however non-binding guidance and is not enforceable.
Many Permits and enforcement actions are beginning to include conditions pertaining to waste minimization. Check to see if those conditions exist, and if so, verify that the facility is in compliance with the conditions.

## Slide 10: OUTREACH
1. Inform generators of available literature and any technical assistance programs.
• ORD Industrial Guides
• State Technical Assistance Programs
• Trade Associations
• Other . . .
2. Give limited, basic advice to the facility of obvious ways that they can minimize their waste.
Notes: As informed inspectors, you should be familiar with different examples of waste minimization literature and recommend these to the facility. Several examples are:
- Facility Pollution Prevention Guide Published by EPA ORD
- Waste Minimization: Environmental Quality with Economic Benefits a little pamphlet published by OSW.
- Any State or Regional Literature available.
Many of these books or pamphlets are free for distribution and if a facility is interested you can supply these for them.
You should also be aware of any technical assistance programs in the area offered either by the Region, the State or the community. Many of these are helpful for information on either very easy or very complex pollution prevention methods. Examples include: EPA compliance assistance centers for Printers, Agriculture, Metal Finishing, Automotive (planned centers for Small Chemical Manufacturing, Printed Wiring Board); and sector notebooks (See, generally, Envirosense at http://es.inel.gov).